## Slide 1
ECOLIGHT MAESTRO
Time & Light Intensity Based Street Light Automation using LPC2129 ARM7
Ajay Manda
B.Tech, Electrical & Electronics Engineering | Godavari Institute of Engineering and Technology

## Slide 2
The Problem
Conventional street lights stay ON for fixed durations, regardless of actual conditions.
This leads to significant, avoidable energy wastage across cities, campuses, and industrial sites.
2
conditions must BOTH be true
before a light turns on
Ecolight Maestro fixes this with dual-condition automation:
time-of-day scheduling + real-time light sensing.

## Slide 3
Project Objectives
1
Reduce power wastage in street lighting systems
2
Automate operation based on environmental conditions
3
Provide user-friendly RTC configuration
4
Demonstrate ARM7 peripheral integration
5
Implement interrupt-driven embedded design

## Slide 4
Key Features
RTC Management
Time, date & day display with keypad-editable parameters
Intelligent Light Sensing
LDR + ADC for automatic day/night detection
Automatic Control
Dual-condition verification switches LEDs ON/OFF
Keypad Interface
4x4 matrix keypad, menu-driven configuration
Interrupt-Driven
EINT0 gives instant access to the config menu
LCD Monitoring
Live time, date, ADC value & system status

## Slide 5
System Architecture
Keypad
(4x4 Matrix)
LDR Sensor
(via ADC)
LPC2129 ARM7
Decision Logic
(RTC + ADC)
RTC Module
Street LEDs
(ON / OFF)
LCD 16x2
Display
Two inputs (keypad, LDR) plus scheduled RTC data feed the LPC2129's decision logic, which drives the street LEDs and updates the LCD.

## Slide 6
Street Light Decision Logic
LED OFF
Time < 18:00
OR
ADC Value > 300
Example: Time = 14:00:00 -> Result: LED OFF
LED ON
Time >= 18:00
AND
ADC Value <= 300
Example: Time = 19:30:00, ADC = 180 -> Result: LED ON

## Slide 7
System Flow
Initialize
LCD / RTC / ADC
Read Time
& LDR Value
Evaluate
Dual Condition
Drive LEDs
& Update LCD
Check EINT0
-> RTC Menu
The loop repeats continuously; an EINT0 trigger branches into the RTC configuration menu before returning to normal operation.

## Slide 8
RTC Configuration Menu
Triggered via EINT0 (P0.16)
1
Update Hour
2
Update Minute
3
Update Second
4
Update Day
5
Update Date
6
Update Month
7
Update Year
8
Exit Menu

## Slide 9
Applications & Future Enhancements
Applications
• Smart Street Lighting
• Smart Cities
• Campus Lighting
• Industrial Lighting
Future Enhancements
• Wireless Monitoring using IoT
• GSM-Based Fault Reporting
• Solar Powered Street Lights
• Motion Detection for Adaptive Brightness
• Cloud-Based Energy Analytics
• Mobile Application Integration

## Slide 10
Conclusion
Ecolight Maestro pairs RTC-based scheduling with real-time light sensing on the LPC2129 ARM7 platform, cutting unnecessary energy use while giving users direct, keypad-driven control over the clock — a solid, low-cost foundation for future IoT and solar-powered upgrades.
Thank You
Ajay Manda | B.Tech, Electrical & Electronics Engineering